## Slide 1
An Interaction Framework for Multi-domain Unmanned Systems
Collaboration Based on Interoperability Messages
Zhigang Wang*, Chilian Chen, Yongping Zhang, Kai Zhang, Chubing Guo, Yongqiong Yuan
CETC Key Laboratory of Data Link Technology
*E-mail:feitianwzg@163.com
INTRODUCTION
Mission Planning Message
To improve the interoperability of unmanned system and enhance the multi-domain unmanned system collaborative capacity, we propose an interaction framework based on interoperability messages. The interaction framework will help human operator make it easier to control different kinds of multi-domain unmanned systems and make autonomous cooperative between unmanned systems possible.
Index | Data element | Data element description
1 | Message label | Describe the message version, exercise label, message generation time, organization
2 | Mission purpose | Describe the mission purpose,, mission type, start time, end time, duration time
3 | Mission members | Describe the mission index, mission priority, mission member’s type and number, specific task for each unmanned system
4 | Situation | Describe the mission area, restricted area, target location, target bearing, assembly area, safety corridor
5 | Execute method | Describe the waypoint planning, task assignment, task sequence
6 | Command and control | Describe the ground/air/surface control station, command and control, handover
7 | Communication and navigation | Describe the horizon communication, over-the-horizon communication and navigation payloads
Purpose: Distribute pre-plan mission information and re-plan mission information to all unmanned systems .
Autonomous Intelligence Message
Collaboration Interoperability Message
Purpose: set the algorithm and the rule parameters used in the mission processing unit.
The inputs and outputs of an algorithm
The conditions and actions of a behavior rule
Purpose: exchange necessary status and collaboration information for mission execution collaboratively.
Index | Message type | Message description
1 | Platform status message | Used to provide the unmanned systems’ platform information, including id, type, position, posture, speed, course.
2 | Payload status message | Used to provide the payloads’ status information, including platform id, payload id, type, work status, core parameters setting.
3 | Mission status message | Used to provide the unmanned systems’ mission information, including platform id, mission id, mission type, mission status, mission priority, next mission.
4 | Target reporting message | Used to provide the found target’s information, including target id, target type, target position, speed, course, bearing, threat level.
5 | Obstacle waring message | Used to provide the obstacle’s information, including obstacle position, obstacle height, obstacle type, influence radius, avoidance methods.
6 | Mission assignment message | Used to assign a mission to a unmanned system by a leader, including sending platform id, receiving platform id, mission type, mission id, mission priority, start time.
7 | Waypoint update message | Used to broadcast a unmanned system’s waypoints if it changes its waypoints, including platform id, waypoint number, waypoint position and time limit.
8 | Coordination message | Used to coordinately execute a mission between different unmanned systems, including sending platform id, receiving platform id, mission type, target id, coordination method and time limit.
Index | Data elements | Bit length | value | Description
1 | Receive platform ID | 8 | 1 | The supported max platform number is 256, the current receive platform is 1.
2 | Algorithms /rules index | 10 | 1 | The supported max Algorithms/rules number is 1024, the current algorithms/ rules is 1.
3.1 | GRI | 1 | 1 | The parameter group data elements will recurring.
3.2 | Parameter ID | 8 | 2 | The supported max Parameters is 256, the current parameters is 2.
3.3 | Parameter value |  |  | Parameter’s bit length and value depends on the parameter’s type.
Message format: the variable message format(VMF), which uses FPI, FRI, GPI, GRI to indicate a data element’s presence and recurrence,
Message format: the fixed word format, initial word, extension word,
continuation words
Control Station: distributes detailed mission information to all unmanned systems and monitors the mission execution through received platform status message, payloads status message, mission status messages.
Unmanned Systems: carry out the mission through its autonomous intelligence and exchanging information with other unmanned systems.
Test the interaction framework in the complex mission environment.
Integration new intelligent algorithms and new behavior rules continually.
Design an uniform data elements dictionary of the three categories messages.
FUTURE WORK