## Slide 1: A Novel Method of Beam Compression Based on Artificial Magnetic Conductor Qiang Gao, Bao-Jun Niu, Hong-Bing Sun, and Wen Jiang Science and Technology on Antenna and Microwave Laboratory, Nanjing 210039, China E-mail: gaoqiang512@foxmail.com
Abstract
In this manuscript, a novel method of beam compression is proposed, which is based on artificial magnetic conductor. The artificial magnetic conductor consists of an array of split ring resonators. Located at the front of an antenna element, the array can compress the radiated beam by the magnetic resonance. Validated by simulation, the beamwidth can be compressed by 15% and the radiated gain can be increased by 0.5 dB.
Introduction and Design
With the continuous development of military antennas, radar and communication standards, the characteristics of communication and detection systems are constantly developed in the direction of low cost, high gain, ultra-wideband, etc., which will increase the difficulty in antennas’ designing and optimizing. Along with the development of metamaterials, some innovate and effective method are applied to ameliorate the gain and directivity of the antennas, such as negative permittivity or permeability, zero-refractive-index metamaterials. It is well known that the array of SRRs shows the characteristic of negative permeability, which is called the artificial magnetic conductor. In this manuscript, the magnetic resonance is applied to compress the beamwidth of the “X” shaped antenna, as shown in Fig. 1. The detailed physical dimensions of the SRR is presented in Fig. 2. Fig. 1 The proposed antenna with the SRRs. Fig. 2 The physical dimensions of the SRR.
Conclusion
In this manuscript, a novel method of beam compression is proposed, which is based on artificial magnetic conductor. The artificial magnetic conductor consists of an array of split ring resonators. The array can produce special magnetic resonance to gather the electromagnetic fields. Located at the front of an antenna element, the array can compress the radiated beam by the magnetic resonance. Validated by simulation, the beam width can be compressed by 15% and the radiated gain can be increased by 0.5 dB. The proposed method can be applied in the design of high-gain antenna of communication and detection systems.
Then the far-field radiation patterns are validated at 250MHz and 270MHz. The results are shown in Fig. 5. The beamwidth of half power without the SRRs are 129° and 111°at 250MHz and 270MHz respectively. When loaded with the SRRs, the beamwidth of half power are 110° and 100°respectively. Obviously, the beamwidth has been compressed by 15% in the maximum. And the radiation gain has been raised by 0.5dB. The results verify the feasibility of the proposed method. (a) Fig. 5 The E-plane and H-plane radiation pattern. (a) 250MHz; (b) 270MHz
Science and Technology on Antenna and Microwave Laboratory
Validation of the performance
Fig. 3 displays the reflection and transmission property of the SRR by S11 and S21 parameters. It can be seen that the SRR has a perfect transmission from 200MHz to 300MHz, which is the operation frequency range of the “X” shaped antenna. Thus, the SRRs can compress the beamwidth and raise the gain by the magnetic resonance without effecting the impedance match of the antenna. Fig. 3 The reflection and transmission property. Fig. 4 The distribution of the electromagnetic fields at 250MHz. (a) with the SRRs; (b) without the SRRs To validate the performance of the proposed compression method, the simulation is done by the CST microwave studio. Firstly, the distributions of the electromagnetic fields around the antenna are collected at 250MHz. When loaded with the SRRs and without the SRR, the comparison is displayed in Fig.4. It can be seen that the energy focuses on the antenna dipole when loaded without the SRRs. With the SRRs, the special resonance enables the energy to focus around the SRRs. More central energy can compress the radiated beam and raise the gain of antenna.