## Slide 1: Design of Radome Based on Multi-layer Structure with Wide Transmission Band Jing Xia, Chang Zhou, Hua-yao Li Wuhan Second Ship Design And Research Institute, Wuhan 430205, China E-mail: 1094706091@qq.com
Abstract
The radome is an important component of the antenna system. With the widening of the working frequency band of the antenna, the radome also needs to have the characteristics of wide transmission band, which puts forward higher requirements for the optimization design of the radome. In this paper, the design of radome with a broad passband is realized based on the multilayer structure. First, the transmission characteristics of the multilayer dielectric layer structure are analyzed by using the equivalent transmission line theory, and then the multi-layer structure is optimized and simulated by 3D electromagnetic simulation software. Finally, the design of a wide transmission band radome with oblique incidence stability is realized.
Introduction and Design
With the development of military requirements, the radome needs to have the characteristics of wide transmission band, and its working frequency band needs to cover one or more bands in most cases. The radome of aircraft generally adopts a single-layer inorganic material with good heat resistance and bearing capacity as the design material of the radome. However, the above single-layer radome can only satisfy good transmission characteristics in a small incident angle range and a narrow frequency band. As shown in Fig.1, it is a schematic diagram of the structure of a single-layer radome. Figure 2 shows the transmission characteristic curve of a single-layer quartz composite radome (εr=3.2, tanδ=0.008, thickness h=15mm) obtained by CST simulation. With the increase of the incident angle, the transmittance under the horizontal polarization increases, and the transmittance under the vertical polarization decreases. Fig. 1 The proposed antenna with the SRRs. According to the design idea of the multi-layer radome, on the basis of the single-layer radome as the outer layer, two different dielectric layers are added inside the radome to realize the radome design with asymmetric structure and wide passband. As shown in Fig.3, it is a schematic diagram of the structure of a three-layer radome. For a radome with a multilayer dielectric structure, the equivalent transmission line theory can be used to analyze its electromagnetic wave transmission characteristics. The equivalent circuit model of the radome with the three-layer structure of Fig. 3 is shown in Fig. 4.
Conclusion
In this manuscript, a wide transmission band radome is designed based on an asymmetric multilayer dielectric structure. Firstly, based on the equivalent transmission line theory, an equivalent circuit model of the three-layer radome was established to analyze its transmission characteristics, and then the transmission characteristics were optimized by using CST, and finally a wide transmission band three-layer radome with oblique incidence stability was designed and realized.
Fig. 2 The transmission characteristic curve of a single-layer radome obtained by CST Through the calculation and analysis of the equivalent circuit model.We should believe that the dielectric parameters and thicknesses of the inner two dielectric layers can be adjusted, so that the electromagnetic wave can achieve the best absorption and reflection loss between different dielectric layers, so that the radome can obtain the ideal electromagnetic wave transmission characteristics. Fig. 3 A schematic diagram of the structure of a three-layer radome Fig. 4 The equivalent circuit model of a three-layer radome
Simulation results
Figure 5 shows the three-layer radome simulation model. In CST, an optimization calculation module is provided. In this paper, 5GHz~18GHz is set as the wide working frequency band of the radome, the oblique incidence angle is 0~45°, and the wave transmittance of the radome satisfies: dB(S(2,1))>-1.5dB.The parameters of the dielectric layer of outer layer 1 remain unchanged, and the dielectric constant and thickness of the dielectric layers of inner layer 2 and inner layer 3 are optimized as variables, so that the optimized radome has a transmittance T in a wide frequency band greater than 70 %. Fig. 5 The three-layer radome simulation model in CST The parameters of each dielectric layer are obtained through the above optimization, and the thickness of the inner layer 2 dielectric layer (ε2=2, tanδ=0.005) and the inner layer 3 dielectric layer (ε3=1.3, tanδ=0.005) are 4.8mm respectively. and 6.6mm. Figure 6 shows the wave transmittance curve of the three-layer radome obtained by simulation. When the oblique incident angle is 0~45°, the wave transmittance of the radome in 5GHz~18GHz is greater than -1.5dB. Compared with the single-layer radome shown in Fig.1, the transmission bandwidth has been effectively broadened. Fig. 6 The wave transmittance curve of the three-layer radome obtained by simulation